Specification

| Model No. | 9024F |
| --- | --- |
| System | Video Compression Format | H.264 |
|  | Main Processor | HI3535 |
|  | Video System | NTSC / PAL |
|  | Operation System | Embedded Linux |
| Video | Video Input | 24CH 1080P |
|  | Video Output | 1 x VGA / 1 x HDMI (1920*1080) |
| Audio | Audio Input | 1 |
|  | Audio Output | 1 |
| Recording | Recording Channel | 24CH 1080P Real Time |
|  | Resolution | NTSC – 1080P (1920 x 1080) / 960P (1280 x 960) / 720P (1280 x 720) |
|  |  | PAL - 1080P (1920 x 1080) / 960P (1280 x 960) / 720P (1280 x 720) |
|  | Recording Mode | Manual / Alarm / Video Detection / Continuous |
| Playback | Playback Channel | 4CH 1080P Real Time |
|  | Search Mode | Time / Date / Alarm / Motion Detection / Exact Search |
|  | Playback Mode | Normal Play / Fast Forward / Fast Rewind / Frame by Frame |
|  | Playback Software | General H.264 Player V1.7.0. |
| Alarm | Alarm Input | NO |
|  | Alarm Output | NO |
| Storage | HDD Interface | 2 x SATA Fixed HDD |
|  | Capability | SATA HDD up to 4TB each |
| Backup | USB Disk | 3 x USB 2.0 port |
|  | SNAP Image | NO |
|  | Backup Format | H.264 (only for Playback Software - General H.264 Player V1.7.0.) |
|  | Backup Mode | Network download / Flash USB / movable HDD/SATA HDD / DVD-RW |
| PTZ | PTZ | YES |
|  | Protocol | NO |
| Network | Interface | RJ45 port / 10M / 100M / 1,000Mbps Ethernet |
|  | Protocol | TCP/IP, DHCP, DDNS, DNS, PPPoE, UPNP, NTP, SMTP |
|  | CMS Program | General_CMS_Eng_V3.0.7.7.T (up to 128 Video channels Platform) |
|  | Mobile phone Support | iPhone / iPad, Android, BlackBerry, Symbian, Windows Mobile Pro |
|  | Computer System Support | Windows 2000, XP, Vista, 7, 8 / Mac OS x 10.6/10.7 |
|  | Compatible Browser | Google Chrome, Internet Explorer, Mozilla Firefox, Safari |
|  | 3G/WIFI | YES |
|  | Free DDNS | iCloud Free DDNS Server (P2P) |
|  | IP Camera Protocol | ONVIF 2.0 / 2.2 Version Platform Protocol |
|  | Simultaneous Remote Viewers | 6 Users Online |
| Others | Operating Temperature | 0°C ~ 55°C |
|  | Operating Humidity | 10% ~ 90% |
|  | Dimension | 300*235*45mm |
|  | Weight | 2.40 KGS |
|  | USB Mouse | YES |
|  | CD Software Disk | YES |
|  | User Manual | YES |
|  | HDD Screw | 8 PCS |
|  | Power Supply | DC12V/4A Power Adapter |

# Text boxes

24-CH

1080P NVR