### A6NS、A4NS

A6NS:A1X04NS、A6X04NS；   A4NS:A7X04NS/NSA、A8X04NSA

（To prevail in kind）

Feature：

- Step on the Internet：With XM cloud service, easy to achieve a variety of network penetrations ,one step to remote monitoring, getting rid of various complicated network settings, easy and simple to operate.

- Compression algorithm ideal：H.264 High Profile compression algorithm,30% decrease of stream due to advanced space-time filtering technology.

- Playback quality: Supports full real-time encoding video, full real-time playback of multi-channel synchronous decoding.

- Main and Sub Stream：Main stream and Sub-stream encoding. Main stream for local storage, ensure image quality; Sub-stream for real-time network transmission, easy to solve bandwidth bottleneck problem.

- Mobile monitor: Support various mobile monitoring（iPhone, Windows Mobile, BlackBerry, Symbian, Android）.

- Display: support VGA, HDMI HD output.

- Operation interface：Similar to Windows operating style, easy to get started with powerful mouse right-click function.

- Network：Powerful network services (support DHCP, PPPOE, FTP, DNS, DDNS, EMAIL,IP searches etc.) And perfect support (WEB, Client, SDK), easy to achieve interoperability.

- Browsers：Support IE、Chrome、Firefox、Safari browsers.

- Remote Access：3322 (Greek network), dyndns, oray (peanut shells), myq-see and other Domain Name Services are also provided.

- Differentiation: Boot screen free replacement, more than twenty languages, over 10 sets of GUI interface, ten kinds of remote control, which make our products different from others.

- Others：With unique black box technology, the whole process can be monitored, which greatly reduces maintenance costs.

Specification：

|  | Model | A6NS | A4NS |
| --- | --- | --- | --- |
| System | Main processor | Hi3520D |
| Video | Video compression | H.264(High Profile) |
|  | Encode capacity | 4*720P/4*AHD-L |
|  | Decode capacity | 1*720P |
|  | Multi-mode input | Pure analog: 4*AHD-M；4*AHD-L |
| Audio | Audio compression | G.711A |
|  | Intercom | support |
| Record & playback | Record mode | manual>alarm>motion detection>timing |
|  | Playback | 1ch |
| Storage & backup | Space occupation | Video:720P 20G / day* channel; 960H 12 ~ 20G / day * channel; Audio: 691.2M / day * channel |
|  | Backup mode | Network, U-disk, USB burner, SATA burner |
| Interface | Video input | 4ch BNC |
|  | Video output | 1ch VGA, 1HDMI |
|  | Audio input | 1ch RCA | 1ch RCA or 4ch RCA |
|  | Audio output | 1ch RCA |
|  | Alarm input | No |
|  | Alarm output | No |
|  | Network interface | RJ45 10M/100M |
|  | PTZ control | No | 1*RS485, Support multiple PTZ protocols |
|  | USB | 2* USB 2.0 |
|  | HDD | 1*SATA port (Max 4TB/per) | 1 or 2*SATA port (Max 4TB/per) |
|  | Wireless | No |
| other | Power supply | 12V/2A | 12V/2A or 12V/4A |